## Slide 1: E/// - URJC CHAIR: Activities 2017 - PROPOSAL
Manuel Lorenzo, Miguel A. Monjas, David Espadas 2017-03-22

## Slide 2: SCOPE & ACTIVITIES KEY CONCEPTS IN FOCUS
DYNAMIC NETWORK SLICE SELECTION
First pre-commercial implementation of a standardized NSSF/P4S assisted by DPI
Implement a few dynamic use cases demonstrating the value of Network Slice selection
Stream Data Processing
Spark Streaming/MLlib
5G
FWA POLICY CONTROL
Enable policy decision in Fixed Wireless Access (FWA) scenarios
Advanced Visualization and Analytics capabilities on the cell congestion information.
Prediction/Longitudinal Data
Spark/Visualization
Mobile Broadband
SECURITY MGT FOR 5G CONNECTED ROBOTICS
Security requirements and associated protection mechanisms that 5G Connected Actionable Devices (Robots) impose on the 5G network
Analytics → Security Analytics seminar pending
Technology → Security Analytics seminar pending
5G/Security/Robotics

## Slide 3: <Dynamic Network Slice Selection> EXECUTIVE SUMMARY
VALUE PROPOSITION Ability of network operators to select an optimized network slice for their customers, based on a combination of historical and real-time inputs. Prototype a pre-commercial NSSF following 3GPP standards. DPI monitors and feeds an Analytics Function, which in turn feeds NSSF. NSSF selects network slice at initial attachment, based on historical data, or asynchronously based on traffic detected by DPI.
BUSINESS ECOSYSTEM Major operators in the 5G arena All operators following 3GPP architectures
OPPORTUNITY Operators to place customers in the best optimized network slice. End customers to be satisfied with the service 3GPP NSSF/P4S is not yet stable in standard. The exact details of functionality are not settled. The interfaces are not yet clear, nor are the protocols to communicate through those interfaces. There is a risk of changes during execution for alignment with the standard.
EXPECTED IMPACT Project success will be measured through the achievements of the following milestones: MS1: Q4/2017: Engagement with operators MS2: Q1/2018: MWC 2018 MS3: Q2/2017-Q2/2018: Influence 3GPP standard
CRITICAL NEEDS Competencies: Policy Control Architectures, DPI, Analytics on Stream Data Infrastructure: Pre-commercial 5G system. Funding: 8 FTE
TEAM Main Stakeholder: Madrid R&D Center Project Driver: Ericsson Project Team: Ericsson, Ericsson Chair URJC

## Slide 4: Dynamic Network Slice Selection System View
Mobile Access Network
Analytics Function
NSSF
Fixed Access Network
Network Slice n
Network Slice 2
Network Slice 1
AMF
AMF: Access and Mobility Management Function
NSSF: Network Slice Selection Function
DPI
DPI
DPI

## Slide 5: Dynamic Network Slice Selection Use Case 1: Content Based Selection
Network Slice n
Mobile Access Network
Analytics Function
NSSF
Fixed Access Network
Network Slice 2
UE attaches to network. AMF interrogates NSSF, which selects slice based on historical data
UE consumes data traffic. DPI reports services/URLs to Analytics Function
Analytics Function reports aggregated services/URLs to NSSF
NSSF determines a better network slice according to user’s data pattern, reports to AMF to provoke network slice reselection
Network Slice 1
Cache
DPI
Cache
DPI
Cache
DPI
AMF
AMF: Access and Mobility Management Function
NSSF: Network Slice Selection Function
DPI: Deep Packet Inspection

## Slide 6: Dynamic Network Slice Selection
IMPROVEMENT OF THE QOE IN 5G NETWORKS THROUGH SMART RESOURCES ASSIGNMENT
ADAPTIVE NETWORK ARCHITECTURES: NVF, SDN, COMPA…
REAL-TIME ANALYTICS: TRAFFIC PATTERNS & RESOURCE ASSIGNMENT
Technologies needed…
TRAFFIC SIMULATION
REAL-TIME TRAFFIC USAGE PATTERNS ANALYSIS AND PREDICTION
DATA-DRIVEN GW RECOMMENDATION MODEL
PROPOSAL
The proposed research has to be performed in a Lab environment as real 5G networks’ data is not available yet…

## Slide 7: Dynamic Network Slice Selection
APPLICATION FRAMEWORK: P4S IN 5G
Python
Apache Spark:
Spark Streaming
Structured Streaming
MLlib
Docker
Traffic Analyzer (Ericsson)
TECHNOLOGY
ANALYTICS
Machine learning / Data Mining
Linear Regression
Logistic Regression (LR)
Multinomial LR
Similarity-Based Learning
Recommender Systems
Support Vector Machines (SVM)
Neural Networks
Genetic Algorithms
Traffic Simulation
Data-driven Gw Recommendation Model
Real-time Traffic Usage Patterns Analysis and Prediction

## Slide 8: < Fixed-Wireless Access Policy Control > EXECUTIVE SUMMARY
VALUE PROPOSITION FWA aims to provide broadband access in areas where fiber deployment is not suitable. FWA requires the implementation of closed-loop policy control, so that it is possible to throttle capabilities of FWA users in congestion situation without hindering MBB users. The FWA Policy Governance Function integrates with Ericsson OSS and Policy Controller while providing status visualization capabilities (locations, insights…) as well. Additionally, it shall be possible to extract insights from historical OSS location information, in order to detect issues in specific locations.
BUSINESS ECOSYSTEM Telefónica Ericsson
OPPORTUNITY Opportunity for Telefónica: Provide BB access in areas where fiber deployment is not suitable. Expand BB coverage without hindering MBB users Opportunity for Ericsson: Extend policy control portfolio. Introduce policy capabilities in Telefónica. Create competence in the analysis of location information.
EXPECTED IMPACT Project success will be measured through the achievements of the following milestones: MS1: T0 + 1M – 1) Understand OSS data source; 2) Specify use cases; 3) Select implementation technologies; 4) agree SAPC interface; 5) draft a first visualization front-end; 6) Definition of Analytics use cases. MS2: T0 + 5M – 1) Implementation of PGF; 2) Integration with Policy Controller. MS3: T0 + ? – Proof-of-concept/Trial deployed and integrated using real data coming from a customer network.
CRITICAL NEEDS Competencies: Visualization, Prediction, LDAP, OSS, Python, Docker… Infrastructure: OpenStack Cloud, Policy Controller simulator Funding: 8 FTE
TEAM Main Stakeholder: GCA Telefónica, PL UDM Project Driver: Ericsson Project Team: M.A. Monjas (E///), H. Jacynycz (URJC)

## Slide 9: < Security mgt for 5g connected robotics > EXECUTIVE SUMMARY
VALUE PROPOSITION 5G Connected Robots (e.g. Connected Cars or any other type of actionable remote devices) will be exposed to a great amount of security threats. Need to investigate the requirements that this imposes on the 5G network, apart from automated protection mechanisms that are a must.
BUSINESS ECOSYSTEM
OPPORTUNITY Opportunity for Ericsson: Understand the implications and requirements imposed on the 5G network in order to ensure secure operation of Connected Robots or IoT devices in general, and means to automate such security
EXPECTED IMPACT Analyze and Explore the Security requirements associated to 5G Connected Robots and understand implications in the 5G network, and figure out how to apply brand-new Security Analytics solutions
CRITICAL NEEDS Competencies: 5G network, Connected Robotics, Connected cars, IoT Expertise Infrastructure: 5G network, Cloud Robotics Platform and robots (e.g. connected cars) Funding: CHARISMA + Addittional Research Funds
TEAM Main Stakeholder: EU Commission (H2020 CHARISMA) Project Driver: Ericsson Project Team: Ericsson, Ericsson Chair URJC
Robotics Industry Partners

## Slide 10: Resources & Effort DATA SCIENCE SCOPE
 | Effort | Team
Dynamic Network Slice Selection | 8 PM | Raúl Sánchez, Nacho Arias E/// Mentor: Miguel A. García URJC Mentor: TBD
Security Management for 5G Connected Robotics | 10 PM | Pablo Nieto, Sameh Dabbour E/// Mentor: Carolina Canales URJC Mentor: TBD
FWA Policy Control | 8 PM | Héktor Jacynycz, M.A. Monjas E/// Mentor: David Espadas URJC Mentor: TBD